## Slide 1: ECE237
ARCHITECTING SMART IOT DEVICES

## Slide 2: Node MCU Pin Configuration

## Slide 3: Getting Started with Node MCU using Arduino IDE
Introduction
Arduino IDE. We can also develop NodeMCU applications using Arduino development environment. This makes things easy for Arduino developers than learning new language and IDE for NodeMCU.

## Slide 4: Let’s see about setting up Arduino IDE with NodeMCU.
First Download Arduino IDE (version 1.6+) https://www.arduino.cc/en/Main/Software
Open Arduino IDE and Go to
File -> Preference.

## Slide 5
Now on Preference window, Enter below link in Additional Boards Manager URLs

## Slide 6
Now close Preference window and go to Tools -> Board -> Boards Manager

## Slide 7
In Boards Manager window, Type esp in the search box, esp8266 will be listed there below. Now select latest version of board and click on install.

## Slide 8
After installation of the board is complete, open Tools->Board->and select NodeMCU 1.0(ESP-12E Module).

## Slide 9
Now Your Arduino IDE is ready for NodeMCU
Example
Let’s see how to write simple serial print sketch using Arduino IDE for NodeMCU.
First connect NodeMCU Development Kit with PC as shown in below figure.

## Slide 11: Node-MCU pin details
The NodeMCU ESP8266 development board comes with the ESP-12E module containing ESP8266 chip having Tensilica Xtensa 32-bit LX106 RISC microcontroller .
This microprocessor supports RTOS and operates at 80MHz to 160 MHz adjustable clock frequency.
NodeMCU has 128 KB RAM and 4MB of Flash memory to store data and programs.
Its high processing power with in-built Wi-Fi and Deep Sleep Operating features make it ideal for IoT projects.

## Slide 12
NodeMCU can be powered using Micro USB jack and VIN pin (External Supply Pin). It supports UART, SPI, and I2C interface.

## Slide 13: NodeMCU ESP8266 Specifications & Features
Microcontroller: Tensilica 32-bit RISC CPU Xtensa LX106
Operating Voltage: 3.3V
Input Voltage: 7-12V
Digital I/O Pins (DIO): 16
Analog Input Pins (ADC): 1
UARTs: 1
SPIs: 1
I2Cs: 1
Flash Memory: 4 MB
SRAM: 64 KB
Clock Speed: 80 MHz
USB-TTL based on CP2102 is included onboard, Enabling Plug n Play
PCB Antenna
Small Sized module to fit smartly inside your IoT projects

## Slide 14: NodeMCU Development Board Pinout Configuration
Pin Category | Name | Description
Power | Micro-USB, 3.3V, GND, Vin | Micro-USB: NodeMCU can be powered through the USB port 3.3V: Regulated 3.3V GND: Ground pins Vin: External Power Supply
Control Pins | EN, RST | The pin and the button resets the microcontroller
Analog Pin | A0 | Used to measure analog voltage in the range of 0-3.3V
GPIO Pins | GPIO1 to GPIO16 | NodeMCU has 16 general purpose input-output pins on its board
SPI Pins | SD1, CMD, SD0, CLK | NodeMCU has four pins available for SPI communication.

## Slide 15
UART Pins | TXD0, RXD0, TXD2, RXD2 | NodeMCU has two UART interfaces, UART0 (RXD0 & TXD0) and UART1 (RXD1 & TXD1). UART1 is used to upload the firmware/program.
I2C Pins |  | NodeMCU has I2C functionality support

## Slide 16: PIN Mapping

## Slide 18: On-board Switches & LED Indicator

## Slide 19: Serial Communication

## Slide 20: Serial Communication
You can use the Arduino IDE environment’s built-in serial monitor to communicate with an ESP board.
Click the Tools>>Serial monitor button in the toolbar and select the same baud rate used in the call to begin().

## Slide 21: commonly used serial commands
Serial.begin(9600);
Serial.print(); and Serial.println(): Serial.print prints text on same line. Seial.println puts carriage return at the end of line.
Serial.write();
Serial.available();
Serial.read();

## Slide 22
After setting up Arduino IDE for NodeMCU, open Arduino IDE and write simple sketch of serial print as shown in below figure.

## Slide 23
Ensure that you have selected the correct board as shown in below figure. Also make sure that you have selected the appropriate COM port.

## Slide 24
Now compile & upload the written sketch directly to the NodeMCU Dev Kit by clicking on upload button.

## Slide 25: Practice Program
1. LED blinking without/with Switch
2. LED blinking rate with Potentiometer

## Slide 27: GPIO Input Example:
int ledpin = 5; // D1(gpio5) int button = 4; //D2(gpio4)
int buttonState=0;
void setup() {
pinMode(ledpin, OUTPUT);
pinMode(button, INPUT);
}
void loop() {
buttonState=digitalRead(button); // put your main code here, to run repeatedly:
if (buttonState == 1)
{
digitalWrite (ledpin, HIGH);
delay(200);
}
if (buttonState==0)
{
digitalWrite(ledpin, LOW);
delay(200);
}
}

## Slide 28: Video link
https://www.youtube.com/watch?v=9VEpZlkN0r0
https://www.youtube.com/watch?v=HBSH_x6J1lY

## Slide 30: GPIO Output Example:
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, LOW);
delay(1000); // Wait for a second
digitalWrite(LED_BUILTIN, HIGH); // Turn the LED off by making the voltage HIGH
delay(2000); // Wait for two seconds (to demonstrate the active low LED)
}

## Slide 31: Code for potentiometer led blink