## Slide 1
CAP476:
Data Communication and Networking
Unit-I
Network Basics

## Slide 2: Computer Networks

## Slide 3: Network Topology
Arrangement of networked devices
Shows links, nodes’ layout
Determines data communication paths
Physical or logical network structure
Influences efficiency, reliability

## Slide 4: Types of Topologies
Point-to-Point topology
Bus topology
Star topology
Ring topology
Mesh topology
Tree (Hierarchical) topology
Daisy Chain
Cellular topology
Hybrid Topology

## Slide 5: Point-to-Point topology
Connects exactly two hosts directly
Uses dedicated private communication link
Simple, cost-effective network design
Entire bandwidth reserved for communication
High security with no intermediates

## Slide 6: Bus topology
Devices connect to single cable
Cable is called backbone bus
Data travels entire length cable
Nodes listen for correct address
Terminators stop signal reflections

## Slide 7: Star topology
Devices connect to central hub
Hub controls data transmission
Nodes do not connect directly
Hub can be switch/hub
If hub fails, network fails

## Slide 8: Ring topology
Devices connected in circular loop
Each device connects two neighbors
Data travels one direction only
Each node acts as repeater
Failure breaks entire network

## Slide 9: Mesh topology
Devices connect directly to many
Each node links multiple others
Provides multiple data paths
Supports full and partial mesh
Highly reliable, self-healing network

## Slide 10: Tree (Hierarchical) topology
Devices arranged in hierarchical levels
Root node connects multiple branches
Combines star and bus topologies
Scalable and easy to expand
Failure can isolate segments

## Slide 11: Daisy Chain
Devices connected in linear series
Data travels from one device
Simple, cost-effective network setup
Easy to add new devices
One failure disrupts whole chain

## Slide 12: Cellular topology
Network divided into geographic cells
Each cell served by tower
Frequencies reused in non-adjacent cells
Supports large mobile user numbers
Facilitates wireless communication, roaming

## Slide 13: Hybrid Topology
Combines two or more topologies
Leverages strengths of each type
Flexible and scalable network design
Enhances fault tolerance, reliability
Suitable for diverse network needs