## Slide 1
CAP476:
Data Communication and Networking
Unit-I
TCP/IP model

## Slide 2: TCP/IP model
Developed before OSI model
Consists of four layers
Application layer included upper layers
Layers provide specific functions
Hierarchical protocol modules

## Slide 4: Functions of TCP/IP layer

## Slide 5: Network Access Layer
Combines Physical and Data Link
Defines how data is sent
Transmits data on same network
Encapsulates IP datagram in frames
Uses Ethernet, Token Ring, Frame Relay

## Slide 6: Internet Layer
Second layer of TCP/IP model
Responsible for packet sending
Works regardless of route path
Uses IP, ARP, ICMP protocols
Handles addressing and routing

## Slide 7: Internet Protocol (IP) Functions
Implements logical IP addresses
Host-to-host communication path
Encapsulates data as IP datagram
Fragmentation and reassembly tasks
Routing between distant networks

## Slide 8: Address Resolution Protocol (ARP)
Finds physical address from IP
Network layer protocol function
ARP request broadcasted on network
ARP reply sent by recipient
Physical address cached in memory

## Slide 9: ICMP Protocol
Internet Control Message Protocol
Sends notifications on datagram issues
Informs sender about undeliverable data
Uses ICMP Test and Reply
Reports problems, correction sender's job

## Slide 10: Transport Layer Protocols
Ensures error-free delivery
Facilitates conversation between hosts
Provides interface to network
Includes TCP, UDP, SCTP protocols
Reliable and unreliable service

## Slide 11: User Datagram Protocol (UDP)
Connectionless transport service
Unreliable error detection
Contains source and destination ports
Total length and checksum fields
Does not identify lost packets

## Slide 12: Transmission Control Protocol (TCP)
Reliable, connection-oriented service
Virtual circuit between sender and receiver
Detects and retransmits errors
Segments data with sequence numbers
Reorders segments at destination

## Slide 13: Application Layer
Topmost layer in TCP/IP
Provides network services to users
Handles resource allocation issues
Not an application itself
Interfaces with user applications

## Slide 14: Functions of Application Layer
File transfer, access, management
Email forwarding and storage
Provides directory services globally
Supports network transparency concepts
Manages distributed database sources

## Slide 15: Application Layer Protocols
HTTP: Hypertext Transfer Protocol
SNMP: Network Management Protocol
SMTP: Simple Mail Transfer Protocol
DNS: Domain Name System
TELNET: Terminal Network Protocol/Telecommunication Network

## Slide 16
THANK YOU